## Slide 1: Lecture 03 Data Representation II COMP1411: Introduction to Computer Systems
Dr. Mingsong LYU (呂鳴松)
Department of Computing,
The Hong Kong Polytechnic University
Spring 2023
These slides are only intended to use internally. Do not publish it anywhere without permission.
Acknowledgement: These slides are based on the textbook (Computer Systems: A Programmer’s Perspective) and its slides.

## Slide 2: Overview
Getting familiar with fractional binary numbers
IEEE floating point standard
  Examples and properties
Computation over floating point numbers

## Slide 3: Fractional binary numbers
Fractional decimal numbers
  11.62510 = 1 * 101 + 1 * 100 + 6 * 10-1 + 2*10-2 + 5*10-3
  Precision limitation: 10-3 (0.001)
Fractional binary numbers
  1011.1012 = 1 * 23 + 0 * 22 + 1 * 21 + 1 * 20 + 1 * 2-1 + 0 * 2-2 + 1 * 2-3
  Precision: 2-3 (1/8)
Binary | Decimal
0.001 | 0.125
0.010 | 0.25
0.011 | 0.375
0.100 | 0.5
0.101 | 0.625
0.110 | 0.75
0.111 | 0.875

## Slide 4: Fractional binary numbers
2i
2i-1
4 = 22
2 = 21
1 = 20
2-1 = 1/2
2-2 = 1/4
2-3 = 1/8
2-j
bi | bi-1 | ••• | b2 | b1 | b0 | b-1 | b-2 | b-3 | ••• | b-j
• • •
• • •

## Slide 5: Representable numbers
Limitation #1
  Can only exactly represent numbers of the form x/2k
  Values that cannot be exactly represented:
    1/3 0.0101010101[01]…2
    1/5 0.001100110011[0011]…2
    1/10 0.0001100110011[0011]…2
Limitation #2
  Given a fixed number of bits, limited range of numbers
    More integer bits, or more fraction bits?
    Larger value, or better precision?
    We are running out of bits …
Point here?
Larger value
Point here?
More precise fraction

## Slide 6: Overview
Get familiar with fractional binary numbers
IEEE floating point standard
  Examples and properties
Computation over floating point numbers

## Slide 7: IEEE Floating Point
IEEE Standard 754
  Many machines were having different floating point encodings, hard to exchange information
  In 1985, IEEE established a uniform standard for floating point arithmetic
  Nowadays, supported by all major CPUs
Driven by numerical concerns
  Nice standards for rounding, overflow, underflow
  Hard to make fast in hardware
    Numerical analysts predominated over hardware designers in defining standard

## Slide 8: Floating Point Representation
Numerical form
  Sign bit s determines whether number is negative or positive
  Significand M is normally a fractional value in range [1.0,2.0).
  Exponent E weights value by power of two
Encoding
  Most Significant Bit s is sign bit s
  exp field encodes E (but is not equal to E)
  frac field encodes M (but is not equal to M)
v = (–1)s M 2E
s
exp
frac
31
30
23
22
0
float
63
62
52
51
0
double

## Slide 9: Normalized values - Definition
When: exp ≠ 000…0 and exp ≠ 111…1
E = exp – Bias
  exp: unsigned value read from the exp field
  Bias = 2k-1 -1, where k is the number of bits for exp
    E.g., single precision, k = 8, exp = 1 ~254, E = -126 ~ 127
M = 1.xxx…x2 (with implied leading 1)
  xxx…x: bits from the frac field
  Minimum when frac = 000…0 (M = 1.0)
  Maximum when frac = 111…1 (M = 2.0 - ε)
  (Get extra leading bit for free)
s
exp
frac
v = (–1)s M 2E

## Slide 10: Normalized values - Example
Compute the decimal value of this 32-bit floating point number
  0100 0110 0110 1101 1011 0100 0000 0000
k = 8
S = 0
Significand
  frac = 110110110110100000000002
  M = 1.11011011011012
Exponent
  Exp = 100011002 = 140
  Bias = 27 – 1 = 127
  E = Exp – Bias = 13
0
10001100
11011011011010000000000
v = (–1)s M 2E

## Slide 11: Denormalized values
When: exp = 000…0
E = 1 – Bias (NOT 0 – Bias)
M = 0.xxx…x2 (with implied leading 0)
  xxx…x: bits from the frac field
Cases
  exp = 000…0, frac = 000..0  zero value
    Note that s = 0/1, possitive/negative zero
  exp = 000…0, frac ≠ 000…0  numbers closest to 0.0
s
0000000…0
frac
v = (–1)s M 2E

## Slide 12: Special values
When: exp = 111…1
Case: exp = 111…1, frac = 000…0
  Represents value  (infinity)
  Operation that overflows
    e.g., the result of 1.0/0.0
Case: exp = 111…1, frac ≠ 000…0
  Not-a-Number (NaN)
  Represents case when no numeric value can be determined
    E.g., the result of sqrt(-1),  - ,  × 0
s
1111111…1
frac
v = (–1)s M 2E

## Slide 13: A miniature floating point example
4-bits exp
s
3-bits frac
An 8-bits floating point representation
The smallest non-negative normalized number?
The largest non-negative normalized number?
The smallest non-negative denorm number?
The largest non-negative denorm number?

## Slide 14: A miniature floating point example
s exp frac E Value
0 0000 000 -6 0
0 0000 001 -6 1/8*1/64 = 1/512
0 0000 010 -6 2/8*1/64 = 2/512
…
0 0000 110 -6 6/8*1/64 = 6/512
0 0000 111 -6 7/8*1/64 = 7/512
0 0001 000 -6 8/8*1/64 = 8/512
0 0001 001 -6 9/8*1/64 = 9/512
…
0 0110 110 -1 14/8*1/2 = 14/16
0 0110 111 -1 15/8*1/2 = 15/16
0 0111 000 0 8/8*1 = 1
0 0111 001 0 9/8*1 = 9/8
0 0111 010 0 10/8*1 = 10/8
…
0 1110 110 7 14/8*128 = 224
0 1110 111 7 15/8*128 = 240
0 1111 000 n/a inf
Denormalized
numbers
Normalized
numbers
Special values
4-bits exp
s
3-bits frac
An 8-bits floating point representation
closest to zero
largest denorm
smallest norm
closest to 1 below
closest to 1 above
largest norm

## Slide 15: Visualizing floating point encodings
Only representing discrete numbers in a range
Variable precision: higher as the value is closer to zero
Smooth transition at the boundary of denorm and normalized
+
−
0
+Denorm
+Normalized
−Denorm
−Normalized
+0
NaN
NaN

## Slide 16: Properties
Floating point zero same as integer zero
  All bits are 0
Can (almost) use unsigned integer comparison
  Must first compare sign bits
  Must consider -0 = 0
  NaNs problematic
    Will be greater than any other values
    What should the comparison yield?
  Otherwise OK
    Denorm vs. normalized
    Normalized vs. infinity

## Slide 17: Encoding an integer into the floating point format
Steps
  Normalize to have leading 1
  Round to fit within fraction
  Post-normalize to deal with effects of rounding
Case study
4-bits exp
s
3-bits frac
Value | Binary
128 | 10000000
15 | 00001101
17 | 00010001
19 | 00010011
138 | 10001010
63 | 00111111

## Slide 18: Normalize
Requirement
  Set binary point in the form 1.xxx…x
  Decrement exponent as you shift the point to the left
4-bits exp
s
3-bits frac
Value | Binary | Fraction | E
128 | 10000000 | 1.0000000 | 7
15 | 00001101 | 1.1010000 | 3
17 | 00010001 | 1.0001000 | 4
19 | 00010011 | 1.0011000 | 4
138 | 10001010 | 1.0001010 | 7
63 | 00111111 | 1.1111100 | 5

## Slide 19: Rounding
Round up conditions
  Round = 1, sticky = 1  > 0.5
  Round = 1, sticky = 0  round to even, to make G an even number
1.BBGRXXX
Guard bit: LSB of result
Round bit: 1st bit removed
Sticky bit: OR of remaining bits
Value | Fraction | GRS | Incr? | Rounded
128 | 1.0000000 | 000 | NO | 1.000
15 | 1.1010000 | 100 | NO | 1.101
17 | 1.0001000 | 010 | NO | 1.000
19 | 1.0011000 | 110 | YES | 1.010
138 | 1.0001010 | 011 | YES | 1.001
63 | 1.1111100 | 111 | YES | 10.000
4-bits exp
s
3-bits frac

## Slide 20: Post-normalize
Issue
  Rounding may have caused overflow
  Handle by shifting right once & incrementing exponent
Value | Rounded | exp | Adjust | Result
128 | 1.000 | 7 |  | 128
15 | 1.101 | 3 |  | 15
17 | 1.000 | 4 |  | 16
19 | 1.010 | 4 |  | 20
138 | 1.001 | 7 |  | 144
63 | 10.000 | 5 | 1.000/6 | 64

## Slide 21: Overview
Background: fractional binary numbers
IEEE floating point standard: definition
  Examples and properties
Computation over floating point numbers

## Slide 22: Floating point multiplication
(–1)s1 M1 2E1 x (–1)s2 M2 2E2
Exact Result: (–1)s M 2E
  Sign s: s1 ^ s2
  Significand M: M1 x M2
  Exponent E: E1 + E2
Fixing
  Round M to fit frac precision
  If M ≥ 2, shift M right, increment E
  If E out of range, overflow
Implementation
  The biggest task is multiplying significands
s1
exp1
frac1
s2
exp2
frac2

## Slide 23: Mathematical properties of FP Mult
For the following questions, YES or NO?
Multiplication Commutative (a*b = b*a)?
Multiplication Associative ((a*b)*c = a*(b*c))?
  Possibility of overflow, inexactness of rounding
  Eg: (1e20*1e20)*1e-20= inf, 1e20*(1e20*1e-20)= 1e20
1 * a = a?
Multiplication distributes over addition (a*(b+c) = a*b + a*c)?
  Possibility of overflow, inexactness of rounding
  1e20*(1e20-1e20)= 0.0, 1e20*1e20 – 1e20*1e20 = NaN

## Slide 24: Floating point addition
(–1)s1 M1 2E1 + (-1)s2 M2 2E2
  Assume E1 > E2
Exact Result: (–1)s M 2E
  Sign s, significand M:
    Result of signed align & add
  Exponent E: E2
Fixing
  If M ≥ 2, shift M right, increment E
  if M < 1, shift M left k positions, decrement E by k
  Overflow if E out of range
  Round M to fit frac precision
(–1)s1 M1
(–1)s2 M2
E1–E2
+
(–1)s M
Get binary points lined up

## Slide 25: Mathematical properties of FP addition
For the following questions, YES or NO?
Commutative (a+b = b+a)?
Associative ((a+b)+c = a+(b+c))??
  Overflow and rounding
  (3.14 + 1e20) – 1e20 = 0.0
  3.14 + (1e20 – 1e20) = 3.14
0 is additive identity?
Every element (x) has an additive inverse (exists x’, so that x+x’=0)?
+
−
0
+Denorm
+Normalized
−Denorm
−Normalized
+0
NaN
NaN

## Slide 26
Thank You