## Slide 1: Lecture 06 Processor Architecture COMP1411: Introduction to Computer Systems
Dr. Mingsong LYU (呂鳴松)
Department of Computing,
The Hong Kong Polytechnic University
Spring 2023
These slides are only intended to use internally. Do not publish it anywhere without permission.
Acknowledgement: These slides are based on the textbook (Computer Systems: A Programmer’s Perspective) and its slides.

## Slide 2: Outline
CPU
Design
(LEC06)
How machine instructions are designed
How execution instructions are executed on the HW components
Programmers work
on these levels
(LEC04, LEC05)
C Program
Assembly (X86-64)
Machine Code
CPU Design

## Slide 3: Outline
Instruction Set Design
  Instruction encoding
  exemplified by a miniature X86 ISA
Sequential implementation of processor
CPU Pipelining

## Slide 4: Outline
Instruction Set Design
  Instruction encoding
  exemplified by a miniature X86 ISA
Sequential implementation of processor
CPU Pipelining

## Slide 5: Instruction Set Architecture Design
Designing processor states visible to programmers
Designing a set of instructions
Encoding the instructions
All the above designs will be exemplified by the Y86-64 ISA --- a much simpler X86 ISA enough to demonstrate the key concepts

## Slide 6: Y86-64 processor state
15 64-bit general purpose registers
Conditional codes
  ZF: zero; SF: negative; OF: overflow
Program Counter
  Indicates address of next instruction
Memory
  Byte-addressable storage array
  Words stored in little-endian byte order
RF: Program registers
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%rax
%rcx
%rdx
%rbx
%rsp
%rbp
%rsi
%rdi
CC: Condition codes
PC
DMEM: Memory
Stat: Program status
OF
SF
ZF

## Slide 7: Y86-64 instruction set
0
1
2
3
4
5
6
7
8
9
V
D
D
Byte
pushq rA
A
0
rA
F
jXX Dest
7
fn
Dest
popq rA
B
0
rA
F
call Dest
8
0
Dest
cmovXX rA, rB
2
fn
rA
rB
irmovq V, rB
3
0
F
rB
rmmovq rA, D(rB)
4
0
rA
rB
mrmovq D(rB), rA
5
0
rA
rB
OPq rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0

## Slide 8: Y86-64 instruction set
addq
6
0
subq
6
1
andq
6
2
xorq
6
3
jmp
7
0
jle
7
1
jl
7
2
je
7
3
jne
7
4
jge
7
5
jg
7
6
rrmovq
2
0
cmovle
2
1
cmovl
2
2
cmove
2
3
cmovne
2
4
cmovge
2
5
cmovg
2
6

## Slide 9: Encoding registers
Each register is uniquely specified by a 4-bit ID
ID 15 (0xF) indicates “no register”
%rax
%rcx
%rdx
%rbx
0
1
2
3
%rsp
%rbp
%rsi
%rdi
4
5
6
7
%r8
%r9
%r10
%r11
8
9
A
B
%r12
%r13
%r14
No Register
C
D
E
F

## Slide 10: Instruction examples
Uniqueness (requirement on designing an ISA)
  The encodings must have a unique interpretation
  Given a sequence of bytes (machine code), it can be interpreted into only one valid sequence of instructions
  From the first instruction, always being able to find the start byte of the next instruction
addq %rax, %rbx
6
0
0
3
rrmovq %rax, %r8
2
0
0
8
irmovq 0x36, %rbx
3
0
F
3
36 00 00 00 00 00 00 00
rmmovq %rcx, 0x41c(%rbx)
4
0
1
3
1C 04 00 00 00 00 00 00

## Slide 11: Outline
Instruction Set Design
  Instruction encoding
  exemplified by a miniature X86 ISA
Sequential implementation of processor
CPU Pipelining

## Slide 12: Up to now
Register
file
OF
SF
ZF
PC
OF
ZF
CF
A
L
U
A
B
Compilation
LEC04,05
LEC06
C program
Assembly code
Machine code
Machine code
loaded into memory
LEC06
Execution
How the machine instructions are executed on CPU?

## Slide 13: Stages of instruction execution
Instructions are executed by multiple stages on the CPU
Different instructions follow the same stages
Instruction
memory
PC
increment
CC
ALU
Data
memory
Fetch
Decode
Execute
Memory
Write back
icode, ifun
rA, rB
valC
Register
file
A
B
M
E
PC
valP
srcA, srcB
dstE, dstM
valA, valB
aluA, aluB
Cnd
valE
Addr, Data
valM
PC update
valE, valM
newPC
Stages | Functions
Fetch | Read an instruction from the memory
Decode | Read operands from registers
Execute | Compute value/address
Memory access | Read or write data from/to memory
Write back | Write results to registers
PC update | Update PC, get ready for the next instruction

## Slide 14: Computed values
Stored in CPU on hardware lines/pins
Fetch
  icode Instruction code
  ifun Instruction function
  rA Instr. Register A
  rB Instr. Register B
  valC Instruction constant
  valP Incremented PC
Decode
  srcA Register ID A
  srcB Register ID B
  dstE Destination Register E
  dstM Destination Register M
  valA Register value A
  valB Register value B
Execute
  valE ALU result
  Cnd Branch/move flag
Memory
  valM Value from memory

## Slide 15: Run the machine codes
Use an example program to show how the CPU runs a program in the machine code form
C program
Assembly code
Machine code
loaded into memory

## Slide 16: Run the machine codes
Instruction
memory
PC
increment
CC
ALU
Data
memory
Fetch
Decode
Execute
Memory
Write back
icode, ifun
rA, rB
valC
Register
file
A
B
M
E
PC
valP
srcA, srcB
dstE, dstM
valA, valB
aluA, aluB
Cnd
valE
Addr, Data
valM
PC update
valE, valM
newPC
Stages | irmovq V, rB | irmovq $5, %rsi
Fetch | icode: ifun ← M1[PC] rA:rB ← M1[PC+1] valC ← M8[PC+2] valP ← PC+10 | icode: ifun ← M1[0x018] = 3:0 rA:rB ← M1[0x019] = F:6 valC ← M8[0x01A] = 5 valP ← 0x018 + 10 = 0x022
Decode |  | 
Execute | valE ← 0 + valC | valE ← 0 + 5 = 5
Memory |  | 
Write back | R[rB] ← valE | R[%rsi] ← valE = 5
PC update | PC ← valP | PC ← valP = 0x022

## Slide 17: Run the machine codes
Instruction
memory
PC
increment
CC
ALU
Data
memory
Fetch
Decode
Execute
Memory
Write back
icode, ifun
rA, rB
valC
Register
file
A
B
M
E
PC
valP
srcA, srcB
dstE, dstM
valA, valB
aluA, aluB
Cnd
valE
Addr, Data
valM
PC update
valE, valM
newPC
Stages | irmovq V, rB | irmovq $10, %rdi
Fetch | icode: ifun ← M1[PC] rA:rB ← M1[PC+1] valC ← M8[PC+2] valP ← PC+10 | icode: ifun ← M1[0x022] = 3:0 rA:rB ← M1[0x023] = F:7 valC ← M8[0x024] = 10 valP ← 0x022 + 10 = 0x02C
Decode |  | 
Execute | valE ← 0 + valC | valE ← 0 + 10 = 10
Memory |  | 
Write back | R[rB] ← valE | R[%rdi] ← valE = 10
PC update | PC ← valP | PC ← valP = 0x02C

## Slide 18: Run the machine codes
Instruction
memory
PC
increment
CC
ALU
Data
memory
Fetch
Decode
Execute
Memory
Write back
icode, ifun
rA, rB
valC
Register
file
A
B
M
E
PC
valP
srcA, srcB
dstE, dstM
valA, valB
aluA, aluB
Cnd
valE
Addr, Data
valM
PC update
valE, valM
newPC
Stages | rrmovq rA, rB | rrmovq $rdi, %rax
Fetch | icode: ifun ← M1[PC] rA:rB ← M1[PC+1] valP ← PC+2 | icode: ifun ← M1[0x02C] = 2:0 rA:rB ← M1[0x02D] = 7:0 valP ← 0x02C + 2 = 0x02E
Decode | valA ← R[rA] | valA ← R[%rdi] = 10
Execute | valE ← 0 + valA | valE ← 0 + 10 = 10
Memory |  | 
Write back | R[rB] ← valE | R[%rax] ← valE = 10
PC update | PC ← valP | PC ← valP = 0x02E

## Slide 19: Run the machine codes
Instruction
memory
PC
increment
CC
ALU
Data
memory
Fetch
Decode
Execute
Memory
Write back
icode, ifun
rA, rB
valC
Register
file
A
B
M
E
PC
valP
srcA, srcB
dstE, dstM
valA, valB
aluA, aluB
Cnd
valE
Addr, Data
valM
PC update
valE, valM
newPC
Stages | addq rA, rB | addq $rsi, %rax
Fetch | icode: ifun ← M1[PC] rA:rB ← M1[PC+1] valP ← PC+2 | icode: ifun ← M1[0x02E] = 6:0 rA:rB ← M1[0x02F] = 6:0 valP ← 0x02E + 2 = 0x030
Decode | valA ← R[rA] valB ← R[rB] | valA ← R[%rsi] = 5 valB ← R[%rax] = 10
Execute | valE ← valA + valB Set CC | valE ← 5 + 10 = 15 SF ← 0, ZF ← 0, OF ← 0
Memory |  | 
Write back | R[rB] ← valE | R[%rax] ← valE = 15
PC update | PC ← valP | PC ← valP = 0x030

## Slide 20: Run the machine codes
Instruction
memory
PC
increment
CC
ALU
Data
memory
Fetch
Decode
Execute
Memory
Write back
icode, ifun
rA, rB
valC
Register
file
A
B
M
E
PC
valP
srcA, srcB
dstE, dstM
valA, valB
aluA, aluB
Cnd
valE
Addr, Data
valM
PC update
valE, valM
newPC
Stages | rmmovq rA, D(rB) | rmmovq %rax, 128(%rbp)
Fetch | icode: ifun ← M1[PC] rA:rB ← M1[PC+1] valC ← M8[PC+2] valP ← PC+10 | icode: ifun ← M1[0x030] = 4:0 rA:rB ← M1[0x031] = 0:5 valC ← 128 valP ← 0x030 + 10 = 0x03A
Decode | valA ← R[rA] valB ← R[rB] | valA ← R[%rax] = 15 valB ← R[%rbp] = 0x018
Execute | valE ← valB + valC | valE ← 0x018 + 128 = 0x098
Memory | M8[valE] ← valA | M8[0x098] ← valA = 15
Write back |  | 
PC update | PC ← valP | PC ← valP = 0x03A

## Slide 21: Outline
Instruction Set Design
  Instruction encoding
  exemplified by a miniature X86 ISA
Sequential implementation of processor
CPU Pipelining

## Slide 22: Pipeline
The whole production process is composed of multiple stages
Worker on each stage do only ONE thing
Products line up on the pipeline, each goes through all stages

## Slide 23: Rethinking the sequential machine
Every instruction must go through 6 stages sequentially
In the sequential implementation, when the instruction is in one stage, e.g., execute, all the hardware components in other stages are idle
This is under-utilization of the processor hardware
Instruction
memory
PC
increment
CC
ALU
Data
memory
Fetch
Decode
Execute
Memory
Write back
icode, ifun
rA, rB
valC
Register
file
A
B
M
E
PC
valP
srcA, srcB
dstE, dstM
valA, valB
aluA, aluB
Cnd
valE
Addr, Data
valM
PC update
valE, valM
newPC

## Slide 24: Understanding the performance of pipeline
Executing an instruction consumes 300ps (1ps = 10-12s)
How many instructions can we execute in 1s? (throughput, IPS)
  1/(300 * 10-12) = 3.33 X 109 instructions
Decompose the execution of each instruction into 3 stages, each stage takes 100ps to execute
How many instructions can we execute in 1s? (throughput, IPS)
  1/(100 * 10-12) = 1010
  3 times faster than the sequential execution
Instruction 1
300ps
Instruction 2
300ps
Instruction 3
300ps
I1-S1
100ps
I1-S2
100ps
I1-S3
100ps
I1-S1
100ps
I1-S2
100ps
I1-S3
100ps
I1-S1
100ps
I1-S2
100ps
I1-S3
100ps
I1
I2
I3
time

## Slide 25: Overhead of pipeline
Adding registers between two consecutive pipeline stages
  Each time a clock signal arrives, the result of stage-x will be written to the register between stage-x and stage-(x+1)
  Once the result of stage-x is written, the next stage can start execution with the result as its input
  Accessing registers introduces extra time delay; the end-to-end latency of finishing a single instruction is increased
Stage A
R
E
G
Stage B
R
E
G
Stage C
R
E
G
clock
latency

## Slide 26: Redesign the CPU with pipeline
E
M
W
F
D
Instruction
memory
PC
increment
Register
file
ALU
Data
memory
Select
PC
rB
dstE
dstM
Select
A
ALU
A
ALU
B
Mem.
control
Addr
srcA
srcB
read
write
ALU
fun.
Fetch
Decode
Execute
Memory
icode
data out
data in
A
B
M
E
M_valA
W_valM
W_valE
M_valA
W_valM
d_rvalA
f_pc
Predict
PC
valE
valM
dstE
dstM
Cnd
icode
valE
valA
dstE
dstM
icode
ifun
valC
valA
valB
dstE
dstM
srcA
srcB
valC
valP
icode
ifun
rA
predPC
CC
d_srcB
d_srcA
e_Cnd
M_Cnd
stat
stat
stat
stat
Stat
imem_error
instr_valid
Stat
dstE
dmem_error
m_stat
W_stat
M_stat
E_stat
D_stat
f_stat
Write
back
Stat
Stat

## Slide 27: Bad pipeline design
Nonuniform partitioning
  Latency is determined by the longest stage
Stage A
R
E
G
Stage B
R
E
G
Stage C
R
E
G
clock
50ps
150ps
100ps
A
B
C
B
B
I1
I2
I3
time
A
A
C
C
latency

## Slide 28: Make the pipeline stages uniform
More stages: deep pipeline
More stage registers  more time overhead
Sometimes, a stage cannot be decomposed
Stage
A
R
E
G
Stage
B1
R
E
G
Stage
B2
R
E
G
clock
50ps
50ps
50ps
Stage
B3
R
E
G
Stage
C1
R
E
G
Stage
C2
R
E
G
50ps
50ps
50ps
I1
I2
I3
time
A
B1
B2
B3
C1
C2
A
B1
B2
B3
C1
C2
A
B1
B2
B3
C1
C2

## Slide 29: Data hazard in pipelines
Data dependencies: the results computed by one instruction are used as the data for a following instruction
Data hazard: data dependencies have the potential to cause computation errors by the pipeline

## Slide 30: Data hazard in pipelines
1
2
3
4
5
6
7
8
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
F
D
E
M
W
0x000:
irmovq
$10,%
rdx
0x00a:
irmovq
$3,%
rax
0x014:
addq
%
rdx
,%
rax
0x016: halt
E
D
valA
f
R[
%
rdx
]
=
0
valB
f
R[
%
rax
]
=
0
D
valA
f
R[
%
rdx
]
=
0
valB
f
R[
%
rax
]
=
0
Cycle 4
M
M_
valE
= 10
M_
dstE
=
%
rdx
e_
valE
f
0 + 3 = 3
E_
dstE
=
%
rax
F: fetch
D: decode
E: execute
M: memory
W: write back
Values in %rdx and %rax have not been updated yet, as register update is done in the W stage  incorrect results

## Slide 31: Solution: stalling with nop instructions
0x000: irmovq $10,%rdx
0x00a: irmovq $3,%rax
nop
nop
0x017: addq %rdx,%rax
0x018: halt
nop
1
2
3
4
5
6
7
8
9
F
D
E
M
W
F
D
E
M
W
E
M
W
E
M
W
D
E
M
W
F
D
E
M
W
10
F
E
M
W
11
D
F
D
F
D
F

## Slide 32: Pipeline design
Stalling a pipeline reduces performance
There are other ways to remove the data hazards
There are control hazards, and of course solutions
There are out-of-order pipelines (instruction execution sequence are changed), multi-issue pipelines
……
Pipelines are a key feature to the performance of contemporary powerful CPUs, very complex designs exist

## Slide 33: Summary
Instruction Set Design
  Instruction encoding
  exemplified by a miniature X86 ISA
Sequential implementation of processor
CPU Pipelining

## Slide 34
Thank You